CEMLINE CORPORATION

# CENTRIFUGAL BOILER BLOW OFF TANK

# SPECIFICATION

Centrifugal boiler blow off tank shall be model CBO-___ as manufactured by Cemline Corporation.

Tank shall be ASME Code constructed and stamped for (<=) (>=) 150 psi working pressure and shall be registered with the National Board of Boiler and Pressure Vessel Inspectors.

Vessel shall be furnished with a tangential inlet and a 90 Degree 1/8" minimum thickness type 316 stainless steel wear plate.

Vessel shall have vent opening and inspection openings as required by the ASME Code.

Tank shall have a blacksteel interior with a red oxide prime exterior.

Vessel shall be mounted on angle legs and shall be factory supplied with an integral adjustable water cooling control valve, check valve, and thermometer built into a factory fabricated drain leg which shall cool the condensate.